## Slide 1: PAPER TITLE The Design and Deployment of a Self-Powered, LoRaWAN-Based IoT Environment Sensor Ensemble for Integrated Air Quality Sensing and Simulation
Tunde Awoyinka

## Slide 2: About the Paper
The study presents the design and deployment of a low-cost, self-powered IoT sensor system for measuring particulate matter (PM) in urban areas.
The system uses LoRaWAN for data transmission, is GPS-enabled, and integrates machine learning for calibration.
It operates independently using solar power and adjusts activity based on available energy.
The sensor data feeds into forecasting models and public health monitoring systems.

## Slide 3: LoRaWAN System Design Architecture
LoRaWAN sensing units are comprised of Main Control
Unit (MCU), a Power Control Unit (PCU), an External Sensing Unit (ESU), two power sensors (INA219s), a low-power timer (TPL5110) a solar panel, and a battery
1. Main Controller Unit (MCU)
Uses ATSAMD21G18 microcontroller + LoRaWAN (RHF76-052DM) + GPS (L70).
Handles communication, data collection, and geolocation.
2. Power Control Unit (PCU)
Uses Sunny Buddy (MPPT Solar Charger) to efficiently regulate power from solar panels to battery and MCU.
3. INA219 Power Sensors
Monitor voltage and current from both the battery and the solar panel for power management.
4. Low-Power Timer(TPL5110 )
Minimizes energy consumption by enabling/disabling system operation based on predefined intervals.
5. External Sensing Unit (IPS7100 & BME280)
IPS7100: Optical particle counter for PM and PC data (PM1.0, PM2.5, PM10, PC1.0, PC2.5, PC10).
BME280: Climate sensor (temperature, pressure, humidity) to adjust for environmental biases.

## Slide 4: Operation & Power Management
Operation
Each operation cycle = 15 minutes.
Power availability is checked using INA219 sensors, and a power mode (0–5) is selected based on power availabilty.
In the case of insufficient power, mode 0 (sleep mode) is selected.
For sufficient power, power mode btw (1-5) is selected, and LoRaWAN connection is establish btw the sensor node and the central gateway. i.e. Power Modes determine how often and how long the system samples and transmits data.
Power-saving strategy: More energy = more frequent sampling; low energy = sleep mode.
Power Management
Power mode 1 & 2: has 1 sensing cycle which take 7 min, and then system sleep for 8 (15–7) min to complete a cycle
Power mode 3 & 4: has 2 sensing cycle which take 10 min, sleep for 5min to complete a cycle.
Power mode 5: has infinite sensing cycle, no sleep.

## Slide 5: Communication & Analytical Toolbox
Communication
The End nodes (a): collects the data & send to the central communication nodes / LoRaWAN gateway (b)
LoRaWAN gateway: gather data packets and send them up to a LoRaWAN cloud.
The LoRaWAN Network/Cloud(c): sorted out the data packets, processed and distributed using an MQTT pipeline. The MQTT pipeline is used to cater both the SharedAirDFW public portal(d) and an extensive analytical toolbox(e).
SharedAirDFW portal: provides up-to-date sensor data and made data available to public.
Analytical Toolbox (e)
The toolbox uses:
Node-RED: to easily ingest and process incoming sensor data
in a simple graphical pipeline.
InfluxDB: data injected by Node-RED goes into InfluxDB, a
time-series database optimized for handling high frequency data from thousands of sources for storage.
Grafana: a dashboard visualization. Grafana is then connected to the database to enable dynamic real-time dashboard visualization.

## Slide 6: Sensor Calibration
Low-cost sensors are calibrated against a Federal Equivalent Method (FEM) monitor (BAM 1022).
Calibration involves:
Humidity correction: humidity correction is applied to the input data collected from the IPS7100, utilizing the climate sensor
(BME280).
  Machine learning models: Random Forest performs best.
Input features are particle counts and climate variables.
Challenges and Future Plans/Directions
Range limitations in urban environments are being addressed with higher-power radios and better antenna design.
Plans include:
  Improved solar and battery configurations
  Additional sensor types
  Enhanced machine learning models via mobile lab and environmental chambers.
The (FEM) Monitor (BAM 1022), LoRaWAN and MINTS node continuously collect data 24/7 for eight months.
Blue arrows: represents particulate matter data,
Green arrows: represent data coming from the climate sensor
Red arrow: represent the particulate matter data FEM Monitor Purple arrow: represents the deployment of the trained machine learning model. Finally LoRaWAN node data is then corrected through the trained model