## Slide 1: How to use Power Sensing/Monitoring for IOT System
Tunde Awoyinka & Diego Malagon

## Slide 2: Selection and Integration of Power Sensors
Criteria for selecting appropriate power sensors
accuracy
power consumption
measurement range
Examples of popular sensor options:
Shunt resistor-based sensors (e.g., INA219, INA226)
Others
Hall-effect sensors (e.g., ACS712)
Dedicated power metering ICs (e.g., ADE7753, MCP39F511
ACS712 AC/DC Current Sensor
INA219 DC Current Sensor

## Slide 3: Power Monitoring Circuits and Design
Type of power monitoring circuits:
Voltage sensing circuits using voltage dividers
Current sensing methods (shunt placement, Kelvin connections)
INA219 DC Current Sensor with shunt resistor

## Slide 4: Voltage Sensing circuits using voltage dividers
The Setup:
A voltage divider consists of two resistors (R1 and R2) connected in series across a voltage source. The sensor resistance (Rs) is placed in series with a known reference resistor (R1), forming the voltage divider.

## Slide 5: Voltage Measurement using ADC
Voltage Measurement:
The microcontroller's analog-to-digital converter (ADC) is connected to the center tap of the voltage divider (the junction between the sensor and the reference resistor(R1)).

## Slide 6: Voltage Monitoring
Software
connect the raspberry pi to monitor, or login in pi via SSH.
1)Write the code
1)enter the following command to create a new file named voltage.py and save this file at direction: /home/pi, and then press enter
sudo nano voltage.py
Enter the sample code in new file, the code can be got by executing shell commands.
2)Run python program
sudo python ./voltage.py
3) Test
Connect the DC port to power supply less 16.5V, the monitor would show the voltage value. For example,you will get the value of 3.29V with the a little allowable error when it connect to 3.3v power supply.

## Slide 7: Current sensing methods (shunt placement)
The shunt resistor creates a small voltage drop proportional to the current, which is then measured to determine the current
High-side current sensing connects the sensing resistor(shunt resistor) between the power supply and load. Low side current sensing is between the load and ground.
Normally, the sensed voltage signal (VSEN = ISEN × RSEN) is so small that it needs to be amplified by subsequent op amp circuits (e.g., noninverting amplifier) to get the measurable output voltage (VOUT).
INA219 DC Current Sensor with shunt resistor
Low-side Current Sensing
High-side Current Sensing with Single Op Amp
High-side Current Sensing with Three Op Amp

## Slide 8: Current Sensing Monitoring
Monitoring of the differential voltage directly across the shunt resistor using a fully differential input ADC (Analog to Digital Converter) and Controller
Direct monitoring of the voltage drop across the current sensing resistor using INA226 and Controller

## Slide 9: Microcontroller and Sensor Interfacing

## Slide 10: Using I2C interface with raspberry pi
16 programmable addresses
Senses Bus Voltages from 0 to 26 V
The device uses a single 3- to 5.5-V supply, drawing a maximum of 1 mA of supply current.

## Slide 11
V50 USB battery pack

## Slide 12
V50 USB battery pack

## Slide 13: Data Sampling Techniques
Technique | Good For | Trade-offs
Fixed Interval | General logging | Simple, may miss fast spikes
Moving Average | Noisy signals | Adds small delay
Change Detection | Efficient logging | Might miss small variations

## Slide 17: Voltaic V50 USB Battery Pack
Always On feature provides continuous powering of microcontrollers, sensors, or other devices with low or intermittent power consumption.
can charge a connected device while simultaneously being recharged itself.
offers two USB-A output ports, both with the Always On functionality, allowing for powering multiple devices or different components of an IoT system.